## Slide 1: The rebirth of neuromorphic accelerators
marc.duranton@cea.fr
www.cea.fr

## Slide 2: 1990’s Neurocomputers...
Siemens : MA-16 Chips (SYNAPSE-1 Machine)
  Synapse-1, neurocomputer with 8xM-A16 chips
  Synapse3-PC, PCI board with 2xMA-16 (1.28 Gpcs)
Adaptive Solutions : CNAPS
  SIMD // machine based on a 64 PE chip.
IBM : ZISC
  Vector classifier engine
Philips : L-Neuro
  1st Gen (1991): 16PEs 26 MCps
  2nd Gen (1995): 12 PEs 720 MCps
+ Intel (ETANN), AT&T (Anna), Hitachi (WSI), NEC, Thomson (now THALES), etc…
CEA’s MIND machine
  Hybrid analog/digital: MIND-128
  Fully digital: MIND-1024
…
2
The rebirth of neuromorphic accelerators

## Slide 3: 1990’s Neurocomputers...
Siemens : MA-16 Chips (SYNAPSE-1 Machine)
  Synapse-1, neurocomputer with 8xM-A16 chips
  Synapse3-PC, PCI board with 2xMA-16 (1.28 Gpcs
Adaptive Solutions : CNAPS
  SIMD // machine based on a 64 PE chip.
IBM : ZISC
  Vector classifier engine
Philips : L-Neuro
  1st Gen (1991): 16PEs 26 MCps
  2nd Gen (1995): 12 PEs 720 MCps
+ Intel (ETANN), AT&T (Anna), Hitachi (WSI), NEC, Thomson (now THALES), etc…
CEA’s MIND machine
  Hybrid analog/digital: MIND-128
  Fully digital: MIND-1024
…
3
The rebirth of neuromorphic accelerators

## Slide 4: 1990’s Neurocomputers...
Siemens : MA-16 Chips (SYNAPSE-1 Machine)
  Synapse-1, neurocomputer with 8xM-A16 chips
  Synapse3-PC, PCI board with 2xMA-16 (1.28 Gpcs
Adaptive Solutions : CNAPS
  SIMD // machine based on a 64 PE chip.
IBM : ZISC
  Vector classifier engine
Philips : L-Neuro
  1st Gen (1991): 16PEs 26 MCps
  2nd Gen (1995): 12 PEs 720 MCps
+ Intel (ETANN), AT&T (Anna), Hitachi (WSI), NEC, Thomson (now THALES), etc…
CEA’s MIND machine
  Hybrid analog/digital: MIND-128
  Fully digital: MIND-1024
…
4
The rebirth of neuromorphic accelerators

## Slide 5: 1990’s Neurocomputers...
Siemens : MA-16 Chips (SYNAPSE-1 Machine)
  Synapse-1, neurocomputer with 8xM-A16 chips
  Synapse3-PC, PCI board with 2xMA-16 (1.28 Gpcs
Adaptive Solutions : CNAPS
  SIMD // machine based on a 64 PE chip.
IBM : ZISC
  Vector classifier engine
Philips : L-Neuro
  1st Gen (1991): 16PEs 26 MCps
  2nd Gen (1995): 12 PEs 720 MCps
+ Intel (ETANN), AT&T (Anna), Hitachi (WSI), NEC, Thomson (now THALES), etc…
CEA’s MIND machine
  Hybrid analog/digital: MIND-128
  Fully digital: MIND-1024
…
5
The rebirth of neuromorphic accelerators
Orange video-grading
Chip alignment
Sleep phase analysis
Image compression
Satellite image analysis
LHC 1st level trigger

## Slide 6: Why Neural Networks are back?
Application needs– “big data” lead to process more and more unstructured data such as images, video, natural signals -, and Neural Networks are good machine-learning solutions,
Algorithmic progress - we are now able to “train” deep neural networks-, and they outperform classical approaches for image classification,

## Slide 7: State-of-the-art in image classification
ImageNet classification (Hinton’s team, hired by Google)
  14,197,122 images, 1,000 different classes
  Top-5 17% error rate (huge improvement)
Facebook’s ‘DeepFace’ Program (labs headed by Y. LeCun)
  4.4 million images, 4,030 identities
  97.35% accuracy, vs. 97.53% human performance
From:Y. Taigman, M. Yang, M.A. Ranzato,
“DeepFace: Closing the Gap to Human-Level
Performance in Face Verification”
650,000 neurons
60,000,000 parameters
630,000,000 synapses

## Slide 8: Examples of results (ImageNet)

## Slide 9: Why Neural Networks are back?
Application needs– “big data” lead to process more and more unstructured data such as images, video, natural signals -, and Neural Networks are good machine-learning solutions,
Algorithmic progress - we are now able to “train” deep neural networks-, and they outperform classical approaches for image classification,
Technological - the high level of parallelism of neural networks can now be implemented in silicon-,
Software crisis – Explicitly programming a large set of processors is difficult, Neural Networks replace imperative programming by a “programming” by examples-,

## Slide 10: Deep Neural Networks: state-of-the-art in image recognition
Database | # Images | # Classes | Best score
MNSIT Handwritten digits | 60,000 + 10,000 | 10 | 99.79%
GTSRB Traffic sign | ~ 50,000 | 43 | 99.46%
CIFAR-10 airplane, automobile, bird, cat, deer, dog, frog, horse, ship, truck | 50,000 + 10,000 | 10 | 91.2%
Caltech-101 | ~ 50,000 | 101 | 86.5%
ImageNet | ~ 1,000,000 | 1,000 | Top-5 83%
DeepFace | ~ 4,000,000 | 4,000 | 97.25%
INCREASING COMPLEXITY
“Programming” by example,
Not explicit, imperative programming

## Slide 11: What is a neural network
The « formal » neuron:

## Slide 12: Topology of Neural networks
Connections between formal neurons…
Perceptron
Rosenblatt -- 1957-58
Multi-layer Perceptron
Kohonen Self-Organizing
Maps
Hopfield
And more…

## Slide 13: What is a Deep Network, CNN?
…
…
…
Deep = number of layers >> 1
13
Notes: Stacking of several convolutional layers
Pooling layer: take the maximum value over small input areas, called receptive fields
In the final layer, each neuron correspond to a different input class (1 neuron / class)

## Slide 14: Example of size of a typical CNN
  Neurons: 287,843
  Synapses: 1,388,800 – Total memory: 1.5MB (with 8 bits synapses)
  Connections: 124,121,800
From: D. Ciresan, U. Meier, J. Masci, J. Schmidhuber, Multi-column deep neural network for traffic sign classification, Neural Networks (32), pp. 333-338, 2012
The German Traffic Sign Recognition Benchmark (GTSRB)
43 traffic sign types
> 50,000 images
Near human recognition (> 98%)
14
Notes: 8 layers, 3 conv layers
What are the consequences of having that many synapses & connections?

## Slide 15: Simplifying the computations
Data representation reduction
  Example on the MNIST handwritten digits database (60,000 images)
    Reduction down to 5 bits
    Using simple saturation instead of Tanh
     Recognition rate drop < 0.2%

## Slide 16: Fast and accurate NN exploration
Automated architecture mapping and benchmarking tool flow
3) Analysis of network performances
Learning
Test
Output categories and localization
Recon. rate
Recon. rate
4) CPU, GPU and FPGA-based real-time implementation
 OpenMP
 OpenCL
 HLS FPGA
; Environment
[env]
SizeX=8
SizeY=8
ConfigSection=env.config
[env.config]
ImageScale=0
; First layer (convolutionnal)
[conv1]
Input=env
Type=Conv
KernelWidth=3
KernelHeight=3
NbChannels=32
Stride=1
; Second layer (pooling)
[pool1]
Input=conv1
Type=Pool
PoolWidth=2
PoolHeight=2
NbChannels=32
Stride=2
; Third layer (fully connected)
[fc1]
Input=conv2
Type=Fc
NbOutputs=100
; Output layer (fully connected)
[fc2]
Input=fc1
Type=Fc
NbOutputs=10
1) Deep network builder
2) Learning a database
Xnet software framework

## Slide 17: Optimized DSP for NN: NeuroDSP
Energy efficient HW accelerator
  Design for DNN processing chains
  Supporting also traditional image processing algo.
Clustered SIMD architecture
  Optimized operators for MAC & NL-approximation
First experiments based on an FPGA
Including 3 clusters (96 PEs) & the
full system
  Validation realized on a real CNN application
    Mapped on NeuroDSP & Designed with XNet
    Caltech-101 database, 96% accuracy
  FPGA version is already competitive with existing CPU & GPU solutions
Platform / Prog. Model | Energy efficiency MOPS/W
NeuroDSP (FPGA) | 765
Intel CoreI7 | 27
GPU | 65
Quad ARM A7 | 200
 x3.8 MOPS/W energy efficiency vs Quad ARM A7

## Slide 18: But Neural Networks have other properties
They are inherently tolerant to computation errors
  Good candidate for “approximate computations”
  That fits with natural signal processing, with no “exact algorithm”
Therefore, they don’t necessarily need binary coding
Temporal coding, like “spike coding”, can be energy efficient
  It is also more similar to coding in the nervous system
  Mixed analog/digital implementations can de efficient:
  For a set of five signal applications:
    Hardware accelerator: area cost of 1.63mm2
    only 2.3% of the energy of an Atom-like core
From: Bilel Belhadj, Antoine Joubert, Zheng Li, Rodolphe Héliot, and Olivier Temam. 2013.
Continuous real-world inputs can open up alternative accelerator designs.
SIGARCH Comput. Archit. News 41, 3 (June 2013), 1-12

## Slide 19: Spike-based Coding
layer 1
Correct
Output
29x29 pixels 841 addresses
Pixel brightness
Spiking frequency
V
t
fMIN
fMAX
Rate-based input coding
Time
layer 2
layer 3
layer 4

## Slide 20: SNN Hardware Accelerator
Spiking Neural Network (SNN) hardware accelerator for DSP functions
Combination of Hardware and Software
  Software: Libraries of mathematical functions and a Compiler
  Hardware: SNN circuit composed of Analog Leaky-Integrate and Fire (LIF) neurons
Two test chips implemented in 65nm
  Reptile: 3 tiles of 12 neurons
  Spider: 25 tiles of 12 neurons
Advanced technology nodes
  Comparison of Analog and Digital neurons
  Gain of Analog neuron (less area)

## Slide 21: Also potential for new learning rules
Spike-based processing can also be interesting to implement local learning rules
This can rely on physical phenomenon, not only floating point computations

## Slide 22: Learning from neuroscience: a STDP Primer
post-synaptic Neuron
pre-synaptic Neuron
Neuron
Axon
Dendrite
Electrical
signal
Synapse
Δt = tpost - tpre
Synaptic weight modification (%)
STDP = correlation detector
 Possible learning model of the mind?
tpre
tpost
<
tpre
tpost
<
Causality
Potentiation (LTP)
Anti-Causality
Depression (LTD)

## Slide 23: Principle of STDP on Crossbars of Memristors
First Proposed by Snider(1)
Vpost
Vpre
tpre
t
Vpre
tpost
t
Vpost
t
Vpre
-Vpost
R decreases
-Vth’
tpre
t
tpost
t
t
R increases
Vth
tpre < tpost
tpre > tpost
Neurons
Synaptic weight update through STDP
Pre-synaptic spike
Post-synaptic spike
(feedback)
G. Snider, Nanoscale Architectures, 2008
B. Linares-Barranco et al, Nature Precedings, 2009
V
V
dR
dt
R
Vth
-Vth’

## Slide 24: Can it compute? A 2 synapses’ dog!
Association is made
Food
Bell
Salivation
1 O. Bichler, W. Zhao, F. Alibart, S. Pleutin, S. Lenfant, D. Vuillaume, C. Gamrat, “Pavlov's Dog Associative Learning Demonstrated on Synaptic-like Organic Transistors”, Neural Computation, 2012
2 Pershin, Y.V. & Di Ventra, M. “Experimental demonstration of associative memory with memristive neural networks.” Arxiv 0905.2935 (2009).
Experimental setup for a Pavlovian associative memory based on memristive devices as proposed by Di Ventra et col.2

## Slide 25: Unsupervised learning example
128
128
AER Sensor
16,384 spiking pixels
1st layer
2nd layer
Lateral
inhibition
Lateral
inhibition
……
……
…
Elementary patterns
…
Shapes
…
Objects
Two-layers system
~ 2 million devices with STDP
Hierarchical Architecture Proposal
O. Bichler, D. Querlioz, S. J. Thorpe, J.-P. Bourgoin and C. Gamrat, “Unsupervised Features Extraction from Asynchronous Silicon Retina through Spike-Timing-Dependent Plasticity”, International Joint Conference on Neural Networks IJCNN August 2011
Results
  98% cars detection rate
  High noise tolerance: same detection rate with 50% added noise
  Very High variability immunity: good performances with 20% synaptic variability (> 95% on learned traffic lanes)

## Slide 26: Weights Evolution During Learning
Recorded stimuli
Synaptic maps for 4 neurons on the first layer
Output 1
Output 2
Output 3
Output 4

## Slide 27: Is it feasible? CBRAM memristor test chip
CMOS/CBRAM Co-integration
  130 nm CMOS process
  CBAM technology Ag/ GeS2 / W
Proof of concept circuit
  4*4 Crossbar (1CB)
  4*4 Matrix (1CB – 1T)
Chip under test
Crossbar : 4.72 µm * 4.72 µm
Matrix : 5.15 µm * 7.1 µm

## Slide 28: Novel NVMs-based Architectures
Equivalent
2-PCM synapse
I = ILTP - ILTD
ILTD
ILTP
From spiking pre-synaptic neurons (inputs)
VRD
Spiking post-synaptic neuron (output)
PCM
Crystallization/
Amorphization
CBRAM
Forming/
Dissolution of
conductive filament
Unsupervised cars trajectories extraction
Unsupervised MNIST handwritten digits classification with stochastic learning
O. Bichler et al., “Visual pattern extraction using energy-efficient ’2-PCM synapse’ neuromorphic architecture.” Electron Devices, IEEE Transactions on, 2012
M. Suri et al., “CBRAM devices as binary synapses for low-power stochastic neuromorphic systems: Auditory (cochlea) and visual (retina) cognitive processing applications”, IEDM, 2012 + M. Suri et al., IEDM 2011 + D. Garbin et al., IEDM 2014

## Slide 29: Conclusion: Overview of some trends…
Limit of frequency scaling -> parallelism, multi-cores
Limit of energy density -> simple, small, efficient cores
New devices will be small, but have large dispersion, low reliability -> error tolerant architectures
New NVRAMS -> Co-locating compute and storage
Cost of moving data -> prefer locality, “computing in memory”
  3D interconnect
More and more “natural data processing” -> new compute paradigms, without explicit programming, in hybrid systems
Neural Networks satisfy all theses trends…

## Slide 30: Evolution of computing?
Evolution: Moore and Darwin, similar result?
Finally something that can be named after me!
« The McCulloch-Pitts result puts an end to this. It proves that anything that can be completely and unambiguously put into words is ipso facto realizable by a suitable finite neural network. »
J . Von Neumann, 1951

## Slide 32
Thank you for your attention